## Slide 1: Workshop 2: Using Arduino: Intro to Arduino Control an LED

## Slide 2: Overview:
Learning outcome:
Basics of Arduino programming (C programming, compiling code).
C programming: 45 min
Arduino programming: 20 min
Compiling code: 10 min

## Slide 3: C programming
Go to https://repl.it/languages/c
Go through the Programming-1 workshop

## Slide 5: Programming an Arduino using the Arduino IDE
Teach what an Arduino is
  background information
    how does it work
    what is it
    does it taste good

## Slide 6: What is an Arduino?
Microprocessor. Has programmable pins that allow you to read data from sensors and send data to other

## Slide 7: Pins:
Pins A0-A7
  Analog pins. Can read/write values between 0V and 5V
Pins D2-D13
  Digital pins. Either on or off (5V or 0V)
Need to set a pin to be either an OUTPUT or INPUT in the setup()
ex:
pinMode(A0, OUTPUT);
pinMode(10, INPUT);

## Slide 8: Input pins:
if digital pin (D2-D13)
  digitalRead(pin#) returns the state of the pin
  value either LOW or HIGH (0 or 1)
if analog pin (A0-A7)
  analogRead(pin#) return the state of the pin
    value between 0 and 1023
ex:
pinMode(A0, INPUT);
int x = analogRead(A0);

## Slide 9: Output pins
if digital pin (D2-D13)
  digitalWrite(pin#, value)
    value = HIGH or LOW
if analog pin (A0-A7)
  analogWrite(pin#, value) return the state of the pin
    value between 0 and 255
ex:
pinMode(A0, OUTPUT);
int x = analogRead(A0, 255);