## Slide 1: Workshop 3: Using Arduino: Button matrix. Resistors and analog inputs

## Slide 2: Overview:
- Learning outcome: Using analog inputs to detect small changes in voltage.
- Project: potentiometer + servo
- analog inputs: 10 min
- button matrix: 10 min
- project: 40 min

## Slide 3: Analog pins detect voltages
Voltage between 0 and 5V is mapped to values between 0 and 1023
0V -> 0
1V -> 204
2V -> 409
3V -> 613
4V -> 818
5V -> 1023
analogRead(pin) = (input/5.0)*1023

## Slide 4: Encoding data with resistances
Connect push buttons in parallel to each other between GND and A0, with a different series resistance each.
Start a serial connection with the Arduino, open the serial monitor
  Read from the A0 pin and print the value to the serial connection.
  Pressing different buttons leads to different voltage readings on the A0 pin!
  By cleverly selecting the resistances, you can even differentiate between presses of combinations of buttons!

## Slide 5: Using a variable resistance to control a servo
Use paper. Draw a line with a pencil (has to be thick and wide)
Graphite is conductive, but has resistance. Put the GND pin at the leftmost part of your line and slide the A0 pin across the line
  Resistance changes!
Find the range of resistance caused by your line (serial monitor)
  We will map the analog input to a servo position

## Slide 6: Check out the practice scripts
practice script “servo-example-variable-resistance.ino”
practice script “LED-matrix”