## Slide 1: Workshop 1:Electronic components. Resistors, capacitors, inductors

## Slide 2: Overview:
- Learning outcome: Basics of circuit analysis. Safety when working with electronics.
- Basics of circuit analysis: 30 min

## Slide 3: Voltage and Current
Voltage: electric potential (energy)
  Charge difference
Current: electrons travelling through circuit (matter)
  “Kinetic energy”, in some sense
OHM’s LAW: V = IR
  V = voltage Volts: [V]
  I = current Amps: [A]
  R = resistance Ohms: [Ω]
P = POWER = VI = I^2/R = V^2*R Watts: [w]

## Slide 4: Electrical circuit:
Open/closed circuit
  Current can flow, or not.
Made of branches (components) connected at nodes
  [insert example image]

## Slide 5: Schematic representation
Resistor:
Capacitor:
Inductor:

## Slide 6
Series: Current same for all components, Voltage different
Parallel: Voltage same for all components, Current different

## Slide 7: Basics of circuit analysis: simplifying circuits
Resistors:
  Series: Req = R1+R2
  Parallel: Req = 1/(1/R1 + 1/R2)
Capacitors:
  Series: Ceq = 1/(1/C1 + 1/C2)
  Parallel: Ceq = C1+C2
Inductors:
  Series: Leq = L1+L2
  Parallel: Leq = 1/(1/L1 + 1/L2)

## Slide 8: Exercise 1: Find the current
[Multiple simple R circuits w/ 1 resistor, series, parallel, series + parallel]

## Slide 9: Exercise 2: Find the voltage
[Multiple simple R circuits w/ 1 resistor, series, parallel, series + parallel]

## Slide 10: When will I need to use this?
Ex: HC-05 Bluetooth module:
The RX pin for this module is rated for 3.3V
  The Arduino pins can only output 5V
    Need a voltage divider to turn the 5V into 3.3V
exercise: What resistor ratio would give us the right voltage at the RX pin?

## Slide 11: Useful component: Diodes
One way valve: Allows current to travel freely in one direction, but not in the other
  Used to protect circuit from connecting a power source backwards
  Used to protect circuit from back EMF
  Used to transform AC to DC (e.g: full bridge rectifier)
  There are different types.
    Can find list on GitHub Common Circuits folder